## Slide 1
BROWARD-MIAMI HEALTH INSTITUTE
Venipuncture Standards and Practice
Module 7 | 30-Hour Basic Intravenous Therapy
Expanded instructor presentation
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 2
Learning objectives
MODULE 7
02
Select an appropriate peripheral vein and catheter
Perform aseptic insertion and securement on a task trainer
Assess, maintain, and discontinue a peripheral IV safely
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 3
Site and device selection
MODULE 7
03
Begin distally when appropriate.
Avoid compromised extremities and sites of infection, flexion, poor circulation, or prior complications.
Select the smallest gauge and shortest catheter that can support the ordered therapy.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 4
Aseptic insertion
MODULE 7
04
Perform hand hygiene, prepare and position the patient, apply the tourniquet, cleanse the site with the approved antiseptic, let it dry, stabilize the vein, observe flashback, thread the catheter, and activate sharps protection.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 5
Securement and maintenance
MODULE 7
05
Connect a primed extension aseptically, assess patency without force, secure the catheter, apply and label the dressing, trace tubing, start the ordered therapy, and reassess the site and patient.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 6
Complication cues
MODULE 7
06
Cool swelling suggests infiltration.
Pain, warmth, redness, or a venous cord suggests phlebitis.
Burning or tissue injury with a vesicant suggests extravasation.
Stop unsafe therapy and follow the condition-specific protocol.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 7
Equipment, Tubing, Catheters, and Infusion Devices 1
MODULE 7
07
Common supplies include the ordered solution, administration set, catheter, extension set, needleless connector, antiseptic, tourniquet, flush, transparent or gauze dressing, securement device, labels, gloves/PPE, sharps container, and infusion device.
Inspect packaging, expiration dates, solution clarity, leaks, and medication labels.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 8
Equipment, Tubing, Catheters, and Infusion Devices 2
MODULE 7
08
Macrodrip tubing has a manufacturer-specific drop factor such as 10, 15, or 20 gtt/mL.
Microdrip tubing is typically 60 gtt/mL.
Pumps control volume over time but do not replace patient and site assessment.
Trace and label tubing, keep connections secure, and respond to alarms by assessing the patient first and then the complete system.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 9
Insertion sequence
MODULE 7
09
Verify order, identity, allergies, indication, therapy, and site restrictions.
Explain the procedure, position the patient, perform hand hygiene, gather supplies, and apply PPE.
Select and assess a distal suitable vein; choose an appropriate catheter.
Apply the tourniquet, prepare the site with approved antiseptic, and allow it to dry.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 10
Insertion sequence continued
MODULE 7
10
Stabilize the vein, insert bevel up, observe flashback, lower/advance as taught, thread the catheter, release the tourniquet, occlude safely, activate needle safety, and discard the needle.
Never reinsert the needle into the catheter.
Connect the primed extension, verify patency according to policy, secure without obscuring assessment, apply/label the dressing, initiate ordered therapy, reassess, and document.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 11
Discontinuation
MODULE 7
11
Stop therapy, perform hand hygiene/PPE, remove dressing and catheter gently, apply pressure and dressing, inspect the catheter for intactness, reassess the site, and document.
Escalate any missing fragment immediately.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 12
Local complications
MODULE 7
12
Infiltration: cool, pale, swollen, uncomfortable site; slowed infusion.
Extravasation: vesicant leakage with pain, blistering, tissue injury, or altered sensation.
Phlebitis: pain, erythema, warmth, swelling, or palpable venous cord.
Hematoma/bleeding, occlusion, dislodgement, leakage, nerve injury, and arterial puncture.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 13
Systemic complications
MODULE 7
13
Allergic reaction/anaphylaxis, bloodstream infection/sepsis, fluid overload, speed shock, air embolism, catheter embolism, and transfusion reaction require rapid recognition.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 14
General response
MODULE 7
14
Stop the infusion when indicated, assess airway/breathing/circulation and vital signs, activate emergency response, notify the RN/prescriber, preserve access or equipment as drug-specific protocol requires, position/support the patient, administer ordered treatment, document objective findings/actions/response, and complete an event report when required.
Never force-flush an occluded or compromised device.
Use current orders, facility policy, and authorized scope when applying this information.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80-92; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 15
Practice and competency check
MODULE 7
15
Palpate and select veins on a task trainer
Perform the complete insertion sequence without contamination
Discontinue the catheter and verify that it remains intact
Complete the matching online lesson and assessment before the in-person laboratory.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80; BMHI IVT 030 course content. Online preparation precedes live practice.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.

## Slide 16
Key points
MODULE 7
16
Select an appropriate peripheral vein and catheter
Perform hand hygiene, prepare and position the patient, apply the tourniquet, cleanse the site with the approved antiseptic, let it dry, stabilize the vein, observe flashback, thread the catheter, and activate sharps protection.
Cool swelling suggests infiltration. Pain, warmth, redness, or a venous cord suggests phlebitis. Burning or tissue injury with a vesicant suggests extravasation. Stop unsafe therapy and follow the condition-specific protocol.
Review the course lesson, complete the assessment, and bring questions to the live session.
Notes: Sources: Supplied Basic Intravenous Therapy Certification manual, pages 80; BMHI IVT 030 course content.
Current legal reference: Florida Administrative Code Rule 64B9-12.005, effective July 20, 2023; Florida Statutes section 464.003 (2026). Instructor must verify current institutional policy and current drug/device guidance before use.